## Slide 1: Network Requirements
Eli Dart, Network Engineer
ESnet Science Engagement
Lawrence Berkeley National Laboratory
2014 ESGF and UV-CDAT Conference
Livermore, CA
December 9, 2014

## Slide 2: Overview
ICNWG background and efforts
Network as Instrument
What’s Next?

## Slide 3
International collaboration between NRENs to support researchers in using networks
  ESnet (US), Funet (FI), Internet2 (US), Janet (UK), SURFnet (NL)
2013 program awards included
  Engineering support and expertise for 4 proposals (2 in climate science)
  10G link upgrade for KNMI
Program motivations
  All research is global—especially science
  Data requirements are increasing
  Networks can make an impact to help research progress
International Climate Network Working Group (ICNWG)
  ESGF working group
  Current task is to manage EYR-assisted improvements

## Slide 4: ICNWG purpose and goals
International Climate Network Working Group
  ESGF working group
  Currently congruent with EYR-Global award
  http://icnwg.llnl.gov/
Purpose: improve data transfer performance between major climate data facilities
  Current tools (http/wget) won’t scale to CMIP6 data volumes
  Technologies exist to significantly improve performance
    Science DMZ
    Globus
Near-term goals – replication workflow using GridFTP
  500MB/sec network performance by May 2014
  500MB/sec (4Gbps) disk to disk transfer by August 2014
Longer-term goals
  1GB/sec (8Gbps) disk to disk by August 2015
  2GB/sec (16Gbps) disk to disk by June 2016 (stretch goal)
Notes: Formed December 2013 at ESGF meeting, LLNL as part of ESGF

## Slide 5
…and many more...
Notes: Small portion of the ESGF organizations participating in ICNWG
In Boulder we talked about increasing participation

## Slide 6: ICNWG Progress
Several perfSONAR hosts are up
  https://icnwg.llnl.gov/
  Also http://ps-dashboard.es.net/index.cgi?dashboard=7%3A%20ESnet%20to%20Climate%20Sites
    (go to http://ps-dashboard.es.net/ and select “Climate Sites” from the Dashboards drop-down on the left)
Some DTN testing has been done
Much work remains
  Would be useful to work more closely with replication group
  Significant performance upgrades still needed
Let’s talk a bit about network performance

## Slide 7
Science Traffic Profile is Different
Notes: ESnet has many capabilities that commercial internet providers do not. I’ll speak about just one.
Commodity internet traffic – large flow count, small per-flow bandwidth, diurnal time signature
Science traffic – small flow count, large per-flow bandwidth, workflow-driven time signature

## Slide 8
Physical pipe that leaks water at rate of .0046% by volume.


Network ‘pipe’ that drops packets at rate of .0046%.


Result
100% of data transferred, slowly, at <<5% optimal speed.
Elephant Flows Place Great Demands on Networks
Result 99.9954% of water transferred.
essentially fixed
determined by speed of light
With proper engineering, we can minimize packet loss.
Assumptions: 10Gbps TCP flow, 80ms RTT.
See Eli Dart, Lauren Rotman, Brian Tierney, Mary Hester, and Jason Zurawski. The Science DMZ: A Network Design Pattern for Data-Intensive Science. In Proceedings of the IEEE/ACM Annual SuperComputing Conference (SC13), Denver CO, 2013.
Notes: It turns out a network has to be almost perfect in order to move the elephant flows effectively.
This is a little bit counterintuitive.
We have to take special care in engineering for the elephant flows.
Irony: van jacobsen 1986 – 88.
This is why a network specifically engineered for science is important

## Slide 9: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: When we solve this problem, the network can be part of the instrument.
This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 10: Network-Centric View of Large Hadron Collider (@CERN)
CERN Computer Center
The LHC Optical Private Network (LHCOPN)
LHC Tier 1 Data Centers
LHC Tier 2 Analysis Centers
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
Universities/
physics groups
The LHC Open Network Environment
(LHCONE)
~50 Gb/s (25Gb/s ATLAS, 25Gb/s CMS)
Level 1 and 2 triggers
O(1-10) meter
O(10-100) meters
O(1) km
1 PB/s
500-10,000 km
Q1: where does “discovery” occur?
LHC Tier 0 Deep archive and send data to Tier 1 centers
detector
Level 3 trigger
Q2: where does the “instrument” end?
Source: Bill Johnston
CERN →T1 | miles | kms
France | 350 | 565
Italy | 570 | 920
UK | 625 | 1000
Netherlands | 625 | 1000
Germany | 700 | 1185
Spain | 850 | 1400
Nordic | 1300 | 2100
USA – New York | 3900 | 6300
USA - Chicago | 4400 | 7100
Canada – BC | 5200 | 8400
Taiwan | 6100 | 9850
Notes: If we take this network-centric view of the LHC (Bill Johnston) it’s even harder to isolate the point of discovery.
Here’s an elaborate international data distribution model.
Two questions: it’s kind of hard to say. Doesn’t appear to be so local.
Clear that discovery is a distributed process. It doesn’t really happen in one singular place: the detector, or at the cluster. Or simply the mind of the physicist.
The network is more than an infrastructure here. It’s part of a distributed instrument for discovery.

## Slide 11: Evolution of LHC Data Model
In chronological order:
Copy as much data as feasible to analysis centers worldwide, with hierarchical distribution.
Relax the hierarchy and rely on caching.
Use “federated data stores” to fetch portions of relevant data sets from remote storage (anywhere), just before they’re needed.
Increasing faith in global science networks.
Notes: This remote IO model is taking hold in HEP, and will in other disciplines.
It is much, much cheaper to move data than to store it twice.

## Slide 12: What Comes Next?
CMIP6
  Still being finalized
  Possible data scale: 4x or 5x larger than CMIP5 (CMIP6: ~10PB)
  Performance improvements needed for data transfer between major sites
Data sets still need to be moved, and will probably need to be moved for some time
There is a need for this – can we do it?
I will argue that we can
  This is not intended to replace server-side analysis
  There is still a need for movement between major sites
  I believe we can meet that need

## Slide 13: Data – How Much Can You Use?
Many scientists don’t have their own HPC facility
  They have an account with an allocation someplace
  XSEDE, DOE, …
Most accounts some with a storage allocation as well
  Disk quota determines easy working set size
  Stay under quota or lots of stuff breaks
  What is the size of a “normal” storage quota?
Say your center offers 10TB of scratch
  If you ask, you can get it increased (up to a point)
  Above 100TB is probably hard (10 such users = 1PB)
Let’s pretend we can get our disk quota raised to 100TB
What is required to move 100TB?

## Slide 14: Sample Data Transfer Rates
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/
Notes: From a 100G perspective, 1TB/hour is trivial – gated completely on end systems
Some collaborations already need 1PB/week – 14Gbps – not much work for 100G network, more work for storage systems

## Slide 15: What Can Be Done With 100TB Of Disk?
What analyses could be done in a 100TB storage envelope?
The future is all up and to the right
  Data volume will increase
  Filesystem capacities will grow
  What does this mean for scientists?
What type of questions do scientists want to ask?
How much data is required to answer those questions?
  Data infrastructure should be able to provide the data on human-reasonable time scales
    What wait time is appropriate?
    100TB/week?
Notes: Even if CMIP6 is not 10EB, data volume still grows

## Slide 16: Vision
  Deploy Science DMZs at the major sites, connected to the science networks
  Major climate modeling centers
  Major data centers
  HPC facilities
This is being done now for the LHC experiments (prep for run 2)
  The LHC folks have been doing this for some time – 3rd architecture now
  Climate can benefit from the experience of the LHC experiments
Make it easy for big data to move
  No worries about the small scale users
  Get the big users what they need
    10s of TB on human-reasonable time scales
    Less human work for data staging
Some climate sites are doing this now – others have more work to do

## Slide 17: Data Performance Engineering For Climate
Data performance team
  ESnet, other networks (JANET, GEANT, AARNet, et. al.)
  Major data centers (PCMDI, NCAR, NASA, NOAA, DKRZ, BADC, ANU/NCI, KNMI, IPSL, etc.)
  Leverage EYR work – expand ICNWG
Center-to-center data performance targets
Regular performance monitoring
This is what the LHC experiments have done – it works
ESnet can help
Notes: This is very operationally-focused

## Slide 18: Thanks!
Eli Dart dart@es.net
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
http://fasterdata.es.net/
http://my.es.net/
http://www.es.net/

## Slide 19: Extra Slides

## Slide 20: Climate CrossConnects – July 2014, Boulder, CO
CrossConnects workshop series
  Bring together scientists, technologists, data managers, senior leadership
  Interactive discussion, working toward strategic advances
Climate CrossConnects
  “Improving Data Mobility & Management for International Climate Science”
  Sponsored by ESnet and Internet2
  Co-sponsors
    Indiana University
    National Center for Atmospheric Research (NCAR)
    National Oceanic and Atmospheric Administration (NOAA)
  Hosted by NOAA in Boulder, CO
    Excellent facility
    Excellent support

## Slide 21: Broad Attendance – 88 People
International
  Americas
  Asia
  Australia
  Europe
Many institutions represented
  Universities
  Research Laboratories
  Mission agencies
  Industry
Special thanks to NSF for travel funds for some attendees
  http://www.nsf.gov/awardsearch/showAward?AWD_ID=1445821&HistoricalAwards=false
Notes: So – what did we learn?

## Slide 22: Climate CrossConnects – Takeaways
We have a bunch of different components
  Many organizations
    Internal missions and external missions
    Research, operations, etc.
    Synergistic interaction with related organizations
  Lots of data
    In many cases data is not where the compute is
    If you can use a subsetting service, fine
    But – no liquid market in fungible computing allocations
      You’ve got cycles where you’ve got cycles
      If the data isn’t already there, need a way to put it there
      The big users have a big problem
Potential for huge progress if this can all be integrated
  How can we do this?

## Slide 23: Progress Under Way
NOAA already has an advanced workflow for managing large-scale data
  Multiple sites
  Fault detection and recovery
  High performance
NASA upgrading its mission infrastructure for observational data
  Instruments produce more data
  Project underway (well-understood – good people on the case)
ESGF data replication upgrades
  Supported by Enlighten Your Research program
    https://www.enlightenyourresearch.net/?page_id=291
    Major ESGF data centers
  Also, ESGF working on Globus integration

## Slide 24: Network Upgrades Matter
Peering moved from 10G link to 100G link
Latency change shows path change
Performance increases
Performance stabilizes
Packet loss goes away
AU-US performance unstable
Low performance in general case
Note packet loss
US-AU performance good, stable

## Slide 25: Where’s the Data?
Data are typically analyzed using computers
This means that in order to do the analysis, the data must be accessible by an application running on the computer
  Usually, that means the computer and the data must be collocated
    Data on a filesystem accessible to applications running on the computer
  This seems obvious, right?
In a lot of cases, moving the data is difficult for users
  #include <perf_litany.h>
“Move the computation to the data!”
  Of course! (if you can…)
  People do this whenever possible (e.g. LHC experiments do this a lot)
  However, this is often not possible. Why?

## Slide 26: Can’t Always Move Compute To Data
A liquid market in fungible HPC allocations does not exist
  Users get an allocation of time and storage on a specific resource
  That allocation is generally not portable
    Account management/security
    Machine architecture, tools, etc.
  In order to use the allocation, user moves data to the computer if it’s not already there
Other reasons as well
  Compute does not always exist near the data (light sources, LHC, etc.)
  Data moves to user-owned compute resource
Therefore, data mobility must be supported by facilities
  Put the data in the right place, regardless of where it is now
  This need will not go away
  The structure of modern science assumes this capability exists
  We need it because we often can’t move the computation to the data

## Slide 27: Protocol Behavior (TCP)
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
How badly does loss affect performance?

## Slide 28: Protocol Behavior (TCP)
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 29: The Science DMZ*: A Network Design Pattern for Data-Intensive Science
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
Last Updated August 18th, 2014
* Science DMZ is a trademark of The Energy Sciences Network (ESnet)

## Slide 30: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 31: Motivation
Networks are an essential part of data-intensive science
  Connect data sources to data analysis
  Connect collaborators to each other
  Enable machine-consumable interfaces to data and analysis resources (e.g. portals), automation, scale
Performance is critical
  Exponential data growth
  Constant human factors
  Data movement and data analysis must keep up
Effective use of wide area (long-haul) networks by scientists has historically been difficult
© 2014, Energy Sciences Network
Notes: Human factors – attention span, ability to manage complexity – these are constant
There is a huge amount of promise in data-intensive science. Effective use of networks can help realize those benefits.
The Science DMZ model helps address the difficulties scientists often experience with using networks.

## Slide 32: Data Mobility in a Given Time Interval
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/
© 2014, Energy Sciences Network
Notes: This succinctly describes what the end to end data path must achieve – network, hosts, storage, application
Green: <= 100Mbps Throughput (almost all domestic locations can do this) – less than Fast Ethernet!
Black: 100Mbps to 10Gbps Throughput (most major research institutions can do this, if its running clean)
Blue 10Gbps to 100Gbps Throughput (emerging at major locations)
Orange > 100Gbps Throughput (future for many)
Note: 1TB/hour and 100TB/week fit easily within 10G of throughput

## Slide 33: The Central Role of the Network
The very structure of modern science assumes science networks exist: high performance, feature rich, global scope
What is “The Network” anyway?
  “The Network” is the set of devices and applications involved in the use of a remote resource
    This is not about supercomputer interconnects
    This is about data flow from experiment to analysis, between facilities, etc.
  User interfaces for “The Network” – portal, data transfer tool, workflow engine
  Therefore, servers and applications must also be considered
What is important? Ordered list:
  Correctness
  Consistency
  Performance
© 2014, Energy Sciences Network
Notes: Networks are key. However, the user interface runs on systems at the edges.
The ordered list of important items is derived from the users of the network:
1) If a tool doesn’t behave correctly, the tool is broken – get another tool
2) If the tool doesn’t behave consistently, I can’t organize my life
3) Among the tools that behave correctly and consistently, choose the tool with the required performance that is easiest to use

## Slide 34: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)
© 2014, Energy Sciences Network
Notes: The application sees the network as a socket.
The socket interface does not provide path diagnostics or other troubleshooting information.
TCP behaves as it does because of measures taken in the 1980s to fix the congestion collapse of the Internet
TCP makes a promise to the application – TCP will get the data to the other end, or TCP will return an error. TCP makes no promises about performance.

## Slide 35: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
© 2014, Energy Sciences Network
Notes: This is an annotated version of the plot from the Science DMZ paper
Beyond your metro area, zero loss is essentially required for high performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 36: Working With TCP In Practice
Far easier to support TCP than to fix TCP
  People have been trying to fix TCP for years – limited success
  Like it or not we’re stuck with TCP in the general case
Pragmatically speaking, we must accommodate TCP
  Sufficient bandwidth to avoid congestion
  Zero packet loss
  Verifiable infrastructure
    Networks are complex
    Must be able to locate problems quickly
    Small footprint is a huge win – small number of devices so that problem isolation is tractable
© 2014, Energy Sciences Network
Notes: Do not underestimate the value of three TCP improvements:
RFC1323 (window scaling)
Kernel autotuning
Improved congestion algorithms
However, loss + latency is still a performance killer.
TCP must be accommodated – this is our job as engineers and architects

## Slide 37: Putting A Solution Together
Effective support for TCP-based data transfer
  Design for correct, consistent, high-performance operation
  Design for ease of troubleshooting
Easy adoption is critical
  Large laboratories and universities have extensive IT deployments
  Drastic change is prohibitively difficult
Cybersecurity – defensible without compromising performance
Borrow ideas from traditional network security
  Traditional DMZ
    Separate enclave at network perimeter (“Demilitarized Zone”)
    Specific location for external-facing services
    Clean separation from internal network
  Do the same thing for science – Science DMZ
© 2014, Energy Sciences Network
Notes: In order to accommodate TCP, we need a pragmatic engineering solution that:
Addresses the needs
Is implementable given financial, policy, and cultural constraints
Can be defended – we cannot ignore security

## Slide 38
Dedicated Systems for Data Transfer
Network Architecture
Performance Testing & Measurement
  Data Transfer Node
High performance
Configured specifically for data transfer
Proper tools
Science DMZ
Dedicated network location for high-speed data resources
Appropriate security
Easy to deploy - no need to redesign the whole network
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
The Science DMZ Design Pattern
© 2014, Energy Sciences Network
Notes: The Science DMZ design pattern is a set of composable ideas, including:
The architectural element itself – the Science DMZ enclave
Appropriate security that does not impact performance
Dedicated systems – Data Transfer Nodes
perfSONAR
The elements of the Science DMZ can be combined in a variety of ways depending on the need

## Slide 39: Abstract or Prototype Deployment
Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk
© 2014, Energy Sciences Network

## Slide 40: Science DMZ Design Pattern (Abstract)
© 2014, Energy Sciences Network
Notes: This is an abstract cartoon – nobody’s network looks exactly like this
The diagram has no management LAN, no terminal servers, etc.
However, this is the minimum network diagram that shows the essential Science DMZ components:
Science DMZ enclave
DTN
perfSONAR (in the WAN, at the border, in the Science DMZ)
Security policy controls

## Slide 41: Local And Wide Area Data Flows
© 2014, Energy Sciences Network
Notes: The green data path is susceptible to TCP performance problems stemming from packet loss combined with long distances
The red data path is very low latency – loss matters much less here (though too much loss will still cause problems)
Remember the throughput vs. latency graph

## Slide 42: Support For Multiple Projects
Science DMZ architecture allows multiple projects to put DTNs in place
  Modular architecture
  Centralized location for data servers
This may or may not work well depending on institutional politics
  Issues such as physical security can make this a non-starter
  On the other hand, some shops already have service models in place
On balance, this can provide a cost savings – it depends
  Central support for data servers vs. carrying data flows
  How far do the data flows have to go?
© 2014, Energy Sciences Network

## Slide 43: Multiple Projects
© 2014, Energy Sciences Network

## Slide 44: Supercomputer Center Deployment
High-performance networking is assumed in this environment
  Data flows between systems, between systems and storage, wide area, etc.
  Global filesystem often ties resources together
    Portions of this may not run over Ethernet (e.g. IB)
    Implications for Data Transfer Nodes
“Science DMZ” may not look like a discrete entity here
  By the time you get through interconnecting all the resources, you end up with most of the network in the Science DMZ
  This is as it should be – the point is appropriate deployment of tools, configuration, policy control, etc.
Office networks can look like an afterthought, but they aren’t
  Deployed with appropriate security controls
  Office infrastructure need not be sized for science traffic
© 2014, Energy Sciences Network

## Slide 45: Supercomputer Center
© 2014, Energy Sciences Network
Notes: Applying the Science DMZ design patterns to a supercomputer center
Note global filesystem – avoids double-copy workflow between DTNs and compute resources
DTNs are not part of major computational resource, and so are not entangled with its config
Science DMZ does not look discrete – however, the elements are here
Firewall appropriately placed
Security for major resources and DTNs implemented in network core
PerfSONAR for performance assurance

## Slide 46: Supercomputer Center Data Path
© 2014, Energy Sciences Network
Notes: DTNs are not part of major computational resource, and so are not entangled with its config
Note virtual circuit path (OSCARS, ION, SDN, etc)

## Slide 47: Major Data Site Deployment
In some cases, large scale data service is the major driver
  Huge volumes of data (Petabytes or more) – ingest, export
  Large number of external hosts accessing/submitting data
Single-pipe deployments don’t work
  Everything is parallel
    Networks (Nx10G LAGs, soon to be Nx100G)
    Hosts – data transfer clusters, no individual DTNs
    WAN connections – multiple entry, redundant equipment
  Choke points (e.g. firewalls) just cause problems
© 2014, Energy Sciences Network

## Slide 48: Data Site – Architecture
© 2014, Energy Sciences Network
Notes: Major data resource (e.g. LHC Tier1)
Lots of parallelism (data transfer clusters)
Firewalls as appropriate
PerfSONAR

## Slide 49: Data Site – Data Path
© 2014, Energy Sciences Network
Notes: The loss-sensitive data path covers the entire network front-end
However – note that the Science DMZ principles are all still here
Especially note security – would you want to drag all this through the enterprise firewall? Far better to do the security in the Science DMZ.

## Slide 50: Distributed Science DMZ
Fiber-rich environment enables a distributed Science DMZ
  No need to accommodate all equipment in one location
  Allows the deployment of institutional science service
WAN services arrive at the site in the normal way
Dark fiber distributes connectivity to Science DMZ services throughout the site
  Departments with their own networking groups can manage their own local Science DMZ infrastructure
  Facilities or buildings can be served without building up the business network to support those flows
Security is more complex
  Remote infrastructure must be monitored
  Several technical remedies exist (arpwatch, no DHCP, separate address space, etc.)
  Solutions depend on relationships with security groups
© 2014, Energy Sciences Network

## Slide 51: Distributed Science DMZ – Dark Fiber
© 2014, Energy Sciences Network
Notes: This provides distributed connectivity to a central Science DMZ

## Slide 52: Multiple Science DMZs – Dark Fiber
© 2014, Energy Sciences Network
Notes: In this case, each Science DMZ can be run separately (e.g. by individual departments or laboratories)

## Slide 53: Development Environment
One thing that often happens is that an early power user of the Science DMZ is the network engineering group that builds it
  Service prototyping
  Deployment of test applications for other user groups to demonstrate value
The production Science DMZ is just that – production
  Once users are on it, you can’t take it down to try something new
  Stuff that works tends to attract workload
Take-home message: plan for multiple Science DMZs from the beginning – at the very least you’re going to need one for yourself
The Science DMZ model easily accommodates this
© 2014, Energy Sciences Network
Notes: Example of workload – ALS DTN became central to most data handling tasks on the beamline within about a month of deployment
The Science DMZ model can easily be replicated because of its modularity

## Slide 54: Science DMZ – Flexible Design Pattern
The Science DMZ design pattern is highly adaptable to research
Deploying a research Science DMZ is straightforward
  The basic elements are the same
    Capable infrastructure designed for the task
    Test and measurement to verify correct operation
    Security policy well-matched to the environment, application set is strictly limited to reduce risk
  Connect the research DMZ to other resources as appropriate
The same ideas apply to supporting an SDN effort
  Test/research areas for development
  Transition to production as technology matures and need dictates
  One possible trajectory follows…
© 2014, Energy Sciences Network
Notes: The next couple are examples of integrating SDN into a DMZ environment
1st it is experimental, then it gradually moves into production.

## Slide 55: Science DMZ – Separate SDN Connection
© 2014, Energy Sciences Network
Notes: Initial deployment brings SDN services to research DMZ via a separate link

## Slide 56: Science DMZ – Production SDN Connection
© 2014, Energy Sciences Network
Notes: Once SDN software for the switch platform is solid and operational models are clear, production Science DMZ supports SDN

## Slide 57: Science DMZ – SDN Campus Border
© 2014, Energy Sciences Network
Notes: When the entire production path supports SDN, SDN is another production service on the Science DMZ and we’re back to the original picture
ESnet5 supports routed traffic and OSCARS on the same platform in a similar way

## Slide 58: Common Threads
Two common threads exist in all these examples
Accommodation of TCP
  Wide area portion of data transfers traverses purpose-built path
  High performance devices that don’t drop packets
Ability to test and verify
  When problems arise (and they always will), they can be solved if the infrastructure is built correctly
  Small device count makes it easier to find issues
  Multiple test and measurement hosts provide multiple views of the data path
    perfSONAR nodes at the site and in the WAN
    perfSONAR nodes at the remote site
© 2014, Energy Sciences Network

## Slide 59: Multiple Ingress Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them
© 2014, Energy Sciences Network
Notes: A brief introduction to the impacts of buffering on network traffic. Key points:
- Host interfaces ‘burst’ at line rate, and then wait (e.g. it’s binary behavior, not a nice steady pacing at some average rate)
- multiple ingress flows behave differently depending on the architecture of the switch. If its ‘shared’ memory, all may be using the same memory buffer. If each interface has its own, then 1 or 2 bursting may be less impactful on the rest of the interfaces.
- buffer bloat is typically not a concern in a Science DMZ

## Slide 60: Router and Switch Output Queues
Interface output queue allows the router or switch to avoid causing packet loss in cases of momentary congestion
In network devices, queue depth (or ‘buffer’) is often a function of cost
  Cheap, fixed-config LAN switches (especially in the 10G space) have inadequate buffering. Imagine a 10G ‘data center’ switch as the guilty party
  Cut-through or low-latency Ethernet switches typically have inadequate buffering (the whole point is to avoid queuing!)
Expensive, chassis-based devices are more likely to have deep enough queues
  Juniper MX and Alcatel-Lucent 7750 used in ESnet backbone
  Other vendors make such devices as well - details are important
  Thx to Jim: http://people.ucsc.edu/~warner/buffer.html
This expense is one driver for the Science DMZ architecture – only deploy the expensive features where necessary
© 2014, Energy Sciences Network
Notes: Goes along with the previous – output is just as important as input

## Slide 61: Output Queue Drops – Common Locations
© 2014, Energy Sciences Network
Notes: In the outbound direction, traffic from the cluster goes from 10G to 1G on the department core switch – the 10G DTN will burst, causing loss if the 1G output queue is too shallow
In the outbound direction, many 1G workstations can congest a single 1G uplink port
In the inbound direction, 10G of WAN traffic goes to a 1G port facing the department core switch – likely loss location (and on the wide area path to the DTN!)
There are a lot of networks with this sort of problem.
The best way to find the problem is to use perfSONAR

## Slide 62: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 63: Performance Monitoring
Everything may function perfectly when it is deployed
Eventually something is going to break
  Networks and systems are complex
  Bugs, mistakes, …
  Sometimes things just break – this is why we buy support contracts
Must be able to find and fix problems when they occur
Must be able to find problems in other networks (your network may be fine, but someone else’s problem can impact your users)
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From RFC793, 1981)
© 2014, Energy Sciences Network
Notes: Remember – TCP promises reliable data delivery, not performance
In order for scientists to see high-performance correct behavior consistently, network engineers must be able to find and fix problems quickly.
Waiting around for trouble tickets is clearly the wrong approach
Not all problems are immediately obvious – many are known as “soft failures”

## Slide 64: Soft Network Failures – Hidden Problems
Hard failures are well-understood
  Link down, system crash, software crash
  Traditional network/system monitoring tools designed to quickly find hard failures
Soft failures result in degraded capability
  Connectivity exists
  Performance impacted
  Typically something in the path is functioning, but not well
Soft failures are hard to detect with traditional methods
  No obvious single event
  Sometimes no indication at all of any errors
Independent testing is the only way to reliably find soft failures
© 2014, Energy Sciences Network
Notes: If something is down hard, it’s easy to find
Soft failures are often visible only from the end systems
This is what makes perfSONAR so valuable – it behaves as an end system behaves, but it measures what the network does
Remember – we want to find the problems BEFORE the users do

## Slide 65: Sample Soft Failures
Rebooted router with full route table
Gradual failure of optical line card
Gb/s
normal performance
degrading performance
repair
one month
© 2014, Energy Sciences Network
Notes: 2 quick examples of soft failures:
The first of these was a Cisco 6509 that had over-filled its route table due to a misconfiguration, but the config had been fixed. The performance problem persisted until the router was rebooted. This could not have been found by auditing the configuration.
The second is a relatively common problem – in a big network there are a lot of pluggable optics packs, and sometimes they just go bad. Often they cause performance problems (soft failure) for a long time before they finally die (hard failure)

## Slide 66: Testing Infrastructure – perfSONAR
perfSONAR is:
  A widely-deployed test and measurement infrastructure
    ESnet, Internet2, US regional networks, international networks
    Laboratories, supercomputer centers, universities
  A suite of test and measurement tools
  A collaboration that builds and maintains the toolkit
By installing perfSONAR, a site can leverage over 1100 test servers deployed around the world
perfSONAR is ideal for finding soft failures
  Alert to existence of problems
  Fault isolation
  Verification of correct operation
© 2014, Energy Sciences Network
Notes: perfSONAR is the gold standard tool for performance testing, measurement, and interdomain troubleshooting in science networks

## Slide 67: perfSONAR Deployment Footprint
© 2014, Energy Sciences Network
Notes: Deployment curve through April 2014

## Slide 68: Lookup Service Directory Search: http://stats.es.net/ServicesDirectory/
© 2014, Energy Sciences Network
Notes: How to find perfSONAR servers and services

## Slide 69: perfSONAR Dashboard: http://ps-dashboard.es.net
© 2014, Energy Sciences Network
Notes: Integrating regular testing into a visualization (ESnet example).
Performance data is public
The tool can trigger alerts to notify NOC staff.
This is a very valuable tool for setting expectations

## Slide 70: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 71: Dedicated Systems – Data Transfer Node
The DTN is dedicated to data transfer
Set up specifically for high-performance data movement
  System internals (BIOS, firmware, interrupts, etc.)
  Network stack
  Storage (global filesystem, Fibrechannel, local RAID, etc.)
  High performance tools
  No extraneous software
Limitation of scope and function is powerful
  No conflicts with configuration for other tasks
  Small application set makes cybersecurity easier
© 2014, Energy Sciences Network
Notes: All aspects of the DTN must be tuned – even the BIOS matters
Limit the scope of the DTN as well – its job is data movement, its job is not to have office software on it.
Craft a specific security profile/policy around its only task.

## Slide 72: Data Transfer Tools For DTNs
Parallelism is important
  It is often easier to achieve a given performance level with four parallel connections than one connection
  Several tools offer parallel transfers, including Globus/GridFTP
Latency interaction is critical
  Wide area data transfers have much higher latency than LAN transfers
  Many tools and protocols assume a LAN
Workflow integration is important
Key tools: Globus Online, HPN-SSH
© 2014, Energy Sciences Network
Notes: DTN is entry point for data from multi-facility workflows – use the right tool for the right job

## Slide 73: Data Transfer Tool Comparison
In addition to the network, using the right data transfer tool is critical
Data transfer test from Berkeley, CA to Argonne, IL (near Chicago). RTT = 53 ms, network capacity = 10Gbps.
    Tool Throughput
    scp: 140 Mbps
    HPN patched scp: 1.2 Gbps
    ftp 1.4 Gbps
    GridFTP, 4 streams 5.4 Gbps
    GridFTP, 8 streams 6.6 Gbps
    Note that to get more than 1 Gbps (125 MB/s) disk to disk requires properly engineered storage (RAID, parallel filesystem, etc.)
© 2014, Energy Sciences Network
Notes: Comparison of legacy and recommended tools.
Note that rsync over HPN-SSH is reasonable in a 1Gbps environment – if you are stuck with rsync over SSH, at least use HPN-SSH.
Globus is now deployed at a large number of major scientific sites – the basic data transfer functionality is free.

## Slide 74: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 75: Science DMZ Security
Goal – disentangle security policy and enforcement for science flows from security for business systems
Rationale
  Science data traffic is simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, financial databases, staff desktops, etc.
  Security controls that are typically implemented to protect business resources often cause performance problems
Separation allows each to be optimized
© 2014, Energy Sciences Network

## Slide 76: Performance Is A Core Requirement
Core information security principles
  Confidentiality, Integrity, Availability (CIA)
  Often, CIA and risk mitigation result in poor performance
In data-intensive science, performance is an additional core mission requirement: CIA  PICA
  CIA principles are important, but if performance is compromised the science mission fails
  Not about “how much” security you have, but how the security is implemented
  Need a way to appropriately secure systems without performance compromises
© 2014, Energy Sciences Network
Notes: You can still have really tight security if you need really tight security – just do it in a way that does not cause performance problems for traffic permitted by policy

## Slide 77: Placement Outside the Firewall
The Science DMZ resources are placed outside the enterprise firewall for performance reasons
  The meaning of this is specific – Science DMZ traffic does not traverse the firewall data plane
  Packet filtering is fine – just don’t do it with a firewall
Lots of heartburn over this, especially from the perspective of a conventional firewall manager
  Lots of organizational policy directives mandating firewalls
  Firewalls are designed to protect converged enterprise networks
  Why would you put critical assets outside the firewall???
The answer is that firewalls are typically a poor fit for high-performance science applications
© 2014, Energy Sciences Network
Notes: Packets do not traverse a firewall device
Firewalls are typically engineered very differently than routers and switches

## Slide 78: Firewall Internals
Typical firewalls are composed of a set of processors which inspect traffic in parallel
  Traffic distributed among processors such that all traffic for a particular connection goes to the same processor
  Simplifies state management
  Parallelization scales deep analysis
Excellent fit for enterprise traffic profile
  High connection count, low per-connection data rate
  Complex protocols with embedded threats
Each processor is a fraction of firewall link speed
  Significant limitation for data-intensive science applications
  Overload causes packet loss – performance crashes
© 2014, Energy Sciences Network
Notes: Each individual processor is typically a fraction of link speed (e.g. eight 1.25Gbps processors for a 10G firewall)

## Slide 79: What’s Inside Your Firewall?
Vendor: “but wait – we don’t do this anymore!”
  It is true that vendors are working toward line-rate 10G firewalls, and some may even have them now
  10GE has been deployed in science environments for over 10 years
  Firewall internals have only recently started to catch up with the 10G world
  100GE is being deployed now, 40Gbps host interfaces are available now
  Firewalls are behind again
In general, IT shops want to get 5+ years out of a firewall purchase
  This often means that the firewall is years behind the technology curve
  Whatever you deploy now, that’s the hardware feature set you get
  When a new science project tries to deploy data-intensive resources, they get whatever feature set was purchased several years ago
© 2014, Energy Sciences Network
Notes: As an element of network design, the enterprise firewall is a poor fit for high-performance scientific applications
Find another way to secure the high-performance scientific applications

## Slide 80: The Firewall State Table
Many firewalls use a state table to improve performance
  State table lookup is fast
  No need to process entire ruleset for every packet
  Also allows session tracking (e.g. TCP sequence numbers)
State table built dynamically
  Incoming packets are matched against the state table
  If no state table entry, go to the ruleset
  If permitted by ruleset, create state table entry
  Remove state table entry after observing connection teardown
Semantically similar to punt-and-switch model of traffic forwarding used on many older routers
© 2014, Energy Sciences Network

## Slide 81: State Table Issues
If the state table is not pruned, it will overflow
  Not all connections close cleanly
    I shut my laptop and go to a meeting
    Software crashes happen
  Some attacks try to fill state tables
Solution: put a timer on state table entries
  When a packet matches the state table entry, update the timer
  If the timer expires, delete the state table entry
What if I just pause for a few minutes?
  This turns out to be a problem – state table timers are typically in the 5-15 minute range, while host keepalive timers are 2 hours
  If a connection pauses (e.g. control channel waits for a large transfer), the firewall will delete the state table entry from under it – the control connection now hangs
  We have seen this in production environments
© 2014, Energy Sciences Network
Notes: Enterprise firewall designers assume that everything is an email, a web browser, or streaming content
Science environments are more complex than that – they make use of the full set of capabilities available
If you violate the assumptions of an enterprise firewall, you experience denial of service – by design!

## Slide 82: Firewall Capabilities and Science Traffic
Firewalls have a lot of sophistication in an enterprise setting
  Application layer protocol analysis (HTTP, POP, MSRPC, etc.)
  Built-in VPN servers
  User awareness
Data-intensive science flows typically don’t match this profile
  Common case – data on filesystem A needs to be on filesystem Z
    Data transfer tool verifies credentials over an encrypted channel
    Then open a socket or set of sockets, and send data until done (1TB, 10TB, 100TB, …)
  One workflow can use 10% to 50% or more of a 10G network link
Do we have to use a firewall?
© 2014, Energy Sciences Network

## Slide 83: Firewalls As Access Lists
When you ask a firewall administrator to allow data transfers through the firewall, what do they ask for?
  IP address of your host
  IP address of the remote host
  Port range
  That looks like an ACL to me!
No special config for advanced protocol analysis – just address/port
Router ACLs are better than firewalls at address/port filtering
  ACL capabilities are typically built into the router
  Router ACLs typically do not drop traffic permitted by policy
© 2014, Energy Sciences Network
Notes: Remember – we have mission requirements for high performance scientific data mobility, and business requirements for cost efficiency.
A firewall mandate is an expensive solution that is a poor match for the task at hand and jeopardizes the scientific mission of the organization.

## Slide 84: Security Without Firewalls
Data intensive science traffic interacts poorly with firewalls
Does this mean we ignore security? NO!
  We must protect our systems
  We just need to find a way to do security that does not prevent us from getting the science done
Key point – security policies and mechanisms that protect the Science DMZ should be implemented so that they do not compromise performance
Traffic permitted by policy should not experience performance impact as a result of the application of policy
© 2014, Energy Sciences Network

## Slide 85: Firewall Performance Example
Observed performance, via perfSONAR, through a firewall:
Observed performance, via perfSONAR, bypassing firewall:
Almost 20 times slower through the firewall
Huge improvement without the firewall
© 2014, Energy Sciences Network
Notes: Real life example, in front of and in back of a firewall that was dramatically impacting performance
perfSONAR is good at finding these issues
Engineers still have to take action to fix the problem

## Slide 86: If Not Firewalls, Then What?
Remember – the goal is to protect systems in a way that allows the science mission to succeed
I like something I heard at NERSC – paraphrasing: “Security controls should enhance the utility of science infrastructure.”
There are multiple ways to solve this – some are technical, and some are organizational/sociological
I’m not going to lie to you – this is harder than just putting up a firewall and closing your eyes
© 2014, Energy Sciences Network
Notes: It will probably work better because the firewall isn’t doing that much for high-performance DTNs anyway

## Slide 87: Other Technical Capabilities
Intrusion Detection Systems (IDS)
  One example is Bro – http://bro-ids.org/
  Bro is high-performance and battle-tested
    Bro protects several high-performance national assets
    Bro can be scaled with clustering: http://www.bro-ids.org/documentation/cluster.html
  Other IDS solutions are available also
Netflow and IPFIX can provide intelligence, but not filtering
Openflow and SDN
  Using Openflow to control access to a network-based service seems pretty obvious
  This could significantly reduce the attack surface for any authenticated network service
  This would only work if the Openflow device had a robust data plane
© 2014, Energy Sciences Network

## Slide 88: Other Technical Capabilities (2)
Aggressive access lists
  More useful with project-specific DTNs
  If the purpose of the DTN is to exchange data with a small set of remote collaborators, the ACL is pretty easy to write
  Large-scale data distribution servers are hard to handle this way (but then, the firewall ruleset for such a service would be pretty open too)
Limitation of the application set
  One of the reasons to limit the application set in the Science DMZ is to make it easier to protect
  Keep desktop applications off the DTN (and watch for them anyway using logging, netflow, etc – take violations seriously)
  This requires collaboration between people – networking, security, systems, and scientists
© 2014, Energy Sciences Network

## Slide 89: Collaboration Within The Organization
All stakeholders should collaborate on Science DMZ design, policy, and enforcement
The security people have to be on board
  Remember: security people already have political cover – it’s called the firewall
  If a host gets compromised, the security officer can say they did their due diligence because there was a firewall in place
  If the deployment of a Science DMZ is going to jeopardize the job of the security officer, expect pushback
The Science DMZ is a strategic asset, and should be understood by the strategic thinkers in the organization
  Changes in security models
  Changes in operational models
  Enhanced ability to compete for funding
  Increased institutional capability – greater science output
© 2014, Energy Sciences Network

## Slide 90: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
Science DMZ Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 91: Science DMZ Superfecta: Engagement
  Data Transfer Node
High performance
Configured for data transfer
Proper tools
perfSONAR
Enables fault isolation
Verify correct operation
Widely deployed in ESnet and other networks, as well as sites and facilities
Science DMZ
Dedicated location for DTN
Proper security
Easy to deploy - no need to redesign the whole network
Performance Testing & Measurement
Dedicated Systems for Data Transfer
Engagement with Network Users
Network Architecture
  Engagement
Partnerships
Education & Consulting
Resources & Knowledgebase
© 2014, Energy Sciences Network
Notes: The trifecta of DMZ, DTN, and perfSONAR is sufficient if your users already understand
If you want to do this right, include user engagement as an integral part of the Science DMZ so that users can be brought in - this is what ESnet does

## Slide 92: Challenges to Network Adoption
Causes of performance issues are complicated for users.
Lack of communication and collaboration between the CIO’s office and researchers on campus.
Lack of IT expertise within a science collaboration or experimental facility
User’s performance expectations are low (“The network is too slow”, “I tried it and it didn’t work”).
Cultural change is hard (“we’ve always shipped disks!”).
Scientists want to do science not IT support
The Capability Gap
© 2014, Energy Sciences Network
Notes: The struggle in engagement – management, engineering, and users often have dug in on bad behavior.
This amounts a capability gap – there is a disconnect from the capabilities of the network and the ability of the scientists to effectively use it
To fix this, we need to get everyone working toward a common goal:
- Management must fund and support the base needs of research
- IT is there to support the users in doing things correctly, and having all components work

## Slide 93: Overview
Science DMZ Motivation and Introduction
Science DMZ Architecture
Network Monitoring
Data Transfer Nodes & Applications
On the Topic of Security
User Engagement
Wrap Up
© 2014, Energy Sciences Network

## Slide 94: Futures
The Science DMZ design pattern is highly adaptable to new technologies
  Software Defined Networking (SDN)
  Non-IP protocols (RDMA over Ethernet)
Deploying new technologies in a Science DMZ is straightforward
  The basic elements are the same
    Capable infrastructure designed for the task
    Test and measurement to verify correct operation
    Security policy well-matched to the environment
    Application set strictly limited to reduce security risk
  Change footprint is small – often just a single router or switch
  The rest of the infrastructure need not change
© 2014, Energy Sciences Network

## Slide 95
The Science DMZ design pattern provides a flexible model for supporting high-performance data transfers and workflows
Key elements:
  Accommodation of TCP
    Sufficient bandwidth to avoid congestion
    Loss-free IP service
  Location – near the site perimeter if possible
  Test and measurement
  Dedicated systems
  Appropriate security
Support for advanced capabilities (e.g. SDN) is much easier with a Science DMZ
Wrapup
© 2014, Energy Sciences Network

## Slide 96: The Science DMZ in 1 Slide
Consists of three key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
© 2014, Energy Sciences Network
Notes: Single slide summary

## Slide 97: Links
  ESnet fasterdata knowledge base
    http://fasterdata.es.net/
  Science DMZ paper
    http://www.es.net/assets/pubs_presos/sc13sciDMZ-final.pdf
  Science DMZ email list
    https://gab.es.net/mailman/listinfo/sciencedmz
  perfSONAR
    http://fasterdata.es.net/performance-testing/perfsonar/
    http://www.perfsonar.net
© 2014, Energy Sciences Network

## Slide 98: Thanks!
Energy Sciences Network (ESnet)
Lawrence Berkeley National Laboratory
http://fasterdata.es.net/
http://my.es.net/
http://www.es.net/

## Slide 99: Extra Slides – Firewall Internals
© 2014, Energy Sciences Network

## Slide 100: Thought Experiment
We’re going to do a thought experiment
Consider a network between three buildings – A, B, and C
This is supposedly a 10Gbps network end to end (look at the links on the buildings)
Building A houses the border router – not much goes on there except the external connectivity
Lots of work happens in building B – so much that the processing is done with multiple processors to spread the load in an affordable way, and results are aggregated after
Building C is where we branch out to other buildings
Every link between buildings is 10Gbps – this is a 10Gbps network, right???
© 2014, Energy Sciences Network
Notes: Go to next slide, speak to the diagram
The text on this slide is for people looking at the deck who are not present at the talk

## Slide 101: Notional 10G Network Between Buildings
© 2014, Energy Sciences Network
Notes: Building A houses the border router – not much goes on there except the external connectivity
Lots of work happens in building B – so much that the processing is done with multiple processors to spread the load in an affordable way, and results are aggregated after
Building C is where we branch out to other buildings

## Slide 102: Clearly Not A 10Gbps Network
If you look at the inside of Building B, it is obvious from a network engineering perspective that this is not a 10Gbps network
  Clearly the maximum per-flow data rate is 1Gbps, not 10Gbps
  However, if you convert the buildings into network elements while keeping their internals intact, you get routers and firewalls
  What firewall did the organization buy? What’s inside it?
  Those little 1G “switches” are firewall processors
This parallel firewall architecture has been in use for years
  Slower processors are cheaper
  Typically fine for a commodity traffic load
  Therefore, this design is cost competitive and common
© 2014, Energy Sciences Network

## Slide 103: Notional 10G Network Between Devices
© 2014, Energy Sciences Network
Notes: Now, convert the buildings into network devices
Building A becomes a border router
Building B becomes a firewall
Building C becomes a core router

## Slide 104: Notional Network Logical Diagram
© 2014, Energy Sciences Network
Notes: If you’re not allowed to look inside, this is all you see
This network is broken, but unless you know to go look you’ll never know why

## Slide 105: Extra Slides – Initial Data Intensive Science Network
© 2014, Energy Sciences Network

## Slide 106: Ad Hoc DTN Deployment
If present, perfSONAR is at the border
  This is a good start
  Need a second one next to the DTN
Entire LAN path has to be sized for data flows
Entire LAN path is part of any troubleshooting exercise
This usually fails to provide the necessary performance.
This is often what gets tried first
Data transfer node deployed where the owner has space
  This is often the easiest thing to do at the time
  Straightforward to turn on, hard to achieve performance
© 2014, Energy Sciences Network
Notes: Call this a ‘converged’ network, its what your local vendor rep will try to sell you
Converged does not work for science – and we can point to the insertion of a fully tuned DTN host as the counter case. The host can work well, but the network won’t due to things like congestion, buffering, security devices, etc.
This is what frustrates users most of all – they bought a new $20k server to run a high-performance tool, and they will be very mad when they get the same performance they would out of something 10 years old using SCP.